## Slide 1
Economic Assessment of Solar Heat for Industrial Process in Tunisia
Filip Schaffitzel
Notes: Good morning to everyone!
I used to be an intern in Frank’s project and I wrote my bachelor thesis about the economics of solar heat for industrial processes in Tunisia. I wrote it in English, that’s why I will also hold this presentation in English and not in French.
Briefly, some information about me: I’m Filip and I studied industrial engineering in Dresden, Germany. I came to Tunisia a year ago with the DAAD, the German Academic Exchange Service. I attended university courses at the ENIT and from March to August I was working as an intern in the DASTII project.
Part of the internship was my bachelor thesis. The goal was to find out about the economics of SHIP investments and to recommend possible policy instruments. My sources were mainly literature and interviews with experts.
Four weeks ago I turned my thesis and now I will present you some of my results.
If you have any questions during the presentation, please feel free to interrupt me and ask.

## Slide 2
Content
Potential
Framework Conditions in Tunisia
Reference Case
Sensitivity Analysis
Policy Instruments
Conclusion
Notes: First, I will briefly talk about the potential of SHIP and the framework conditions in Tunisa.
Then, we will take a look at the economics of a SHIP investment for a reference case.
To find out about the impact of different input parameters, the results of the sensitivity analysis are shown.
Those results also show the biggest financial barriers to SHIP investments. Therefore different financial policy instruments are mentioned to tackle those barriers.
With the conclusion, I will summarize and interpret the results.

## Slide 3
Theoretical Industrial Heat <250 °C | Technical Solar Heat | Source
376.61 | n/a | Reiners, 2011
318.92 | 31.89 | Amous, 2013
1. Potential
Economic Potential?
Notes: Two studies estimated the theoretical potential for SHIP in Tunisia. They used different methods, that‘s why their results differ by about 15%.
Amous estimated also the technical potential using a simulation tool. He took into account further constraints, such available collector area or demand profile.
Both studies show, there is potential. But the question arises whether there is also economic potential for SHIP in Tunisia.

## Slide 4
Current Prices in EUR cents/KWh (incl. VAT) |  | 
Natural Gas | Fuel Oil | Electricity
1.63 | 2.28 | 8.19
2. Framework Conditions in Tunisia
Energy Prices
Policy Instruments
Grants | 30% of investment costs, capped at about 65 EUR/m²
Estimated Annual Increase | 
2015-2021 | 2021-2035
10% | 5%
Notes: In Tunisia, process heat is mainly obtained by the combustion of natural gas and fuel oil. Natural gas for industrial consumers is avaiable at medium and high pressure. High pressure is only used by power plants and industries with high heat demands that are probably not suitable for SHIP integration, as they can use waste heat. Therefore the price of medium pressure was used. This price is at 1.63 EUR cents per kilo watt hour.
For fuel oil there is only one uniform price at 2.28 EUR cents per kilo watt hour.
Energy prices are very low due to high energy subsidies.
Prices are set by the Ministry of Industry. Therefore future price trends depend on future energy policy. In the past 8 years, natural gas prices have increased by 10%. According to International Monetary Fund, the Tunisian government plans to reduce energy subsidies within the next six years. It is therefore assumed that energy prices will increase by 10% per year until 2021. After that a 5% increase is assumed.
Fuel oil has shown similar increases in the past. It is assumed, that it will increase at the same rate as natural gas, because it is also highly subsidized.
If energy prices will increase as exptected. It will lead to an elimination of subsidies in 14 years for natural gas and 20 years for fuel oil.
For SHIP investments, there are currently grants at 30% of the investments costs available. They are capped at 65 EUR per square meter.

## Slide 5
3. Reference Case
Methods of Investment Appraisal
Net Present Value (NPV)
Internal Rate of Return (IRR)
Static Payback Period (SPP)
Input Parameter | Unit | Value
Aperture area | m² | 1000
Lifetime | a | 20
Real discounting factor | % | 7
Inflation per year | %/a | 4.4
Nominal discounting factor | % | 11.7
Notes: To assess the economics of the reference case, the following investment appraisal methods were used:
Net present value, internal rate of return and the static payback period. The static payback period does not discount future cash flows and therefore ignores the time value of money. But according to literature, it is common to use this static value in company practice.
The net present value discounts future net cash flows to the present. For this study a real discounting factor of 7% was chosen. This is eqal to a nominal discounting factor of about 12 % when taking into account inflation.

## Slide 6
3. Reference Case
Assumptions – Cash Outflows
Input Parameter | Unit | FPC | ETC | Concentrating
Specific total investment costs | EUR/m² | 400 | 500 | 550
Equity ratio | % of Cinv | 30 |  | 
Interest rate | % | 7 |  | 
Repayment period | a | 5 |  | 
O&M costs | % of Cinv | 1 | 1 | 1.5
Annual increase | %/a | 0.5 |  | 
Electrical consumption | % | 2 | 2 | 2.5
Notes: A SHIP investment is characterized by cash inflows resutling from fuel savings and cash outflows.
There are three different cash outflows:
the investment costs (aperture area 1000 m²)
Operation and maintenance costs
Costs for electrical consumption
Total investment costs were assumed at 400 EUR/m² for flat plate collectors. 500 for evacuated tube collectors and 550 for concentrating collecotrs. The assumptions were based on literature and information of suppliers for a 1000 square meter plant.
An equity ratio of 30 % is assumed. The remaining 70% of investment costs are financed with a 5-year bank loan with a 7% interest rate.
Operation and maintenance costs are estimated to be at 1 % of investment costs for stationary collectors. Higher O&M costs are assumed for concentrating technologies due to the maintenance of tracking systems and cleaning of the reflectors. As SHIP plants become older, they might require more maintenance. An annual increase of 0.5% is assumed.
The solar system consumes electricity for pumps, valves, and tracking system. Electrical consumption is assumed at 2% of the useful solar yield. For concentrating technologies it is slightly higher due to the additional operation of the tracking system.

## Slide 7
3. Reference Case
Assumptions – Cash Inflows
Solar irradiation
Solar system efficiency
Specific solar yield
Aperture area
Solar yield
Utilization rate
Fuel savings
Fuel prices
Useful solar yield
Boiler efficiency
Cash inflow
Input Parameter | Unit | FPC | ETC | Concentrating
Irradiation (Gtilt, DNI) | kWh/m²/a | 2050 | 2050 | 2000
System efficiency | % of G | 45 | 40 | 40
Annual degradation | %/a | 0.5 |  | 
Utilization rate | % of Qsol | 75 | 75 | 90
Boiler efficiency | % | 85 |  | 
Notes: Cash inflows incur in form of fuel savings. The upper graph illustrates the calculation of the cash inflow.
For stationary collectors the irradiation on a tilted plane is relevant. It is about 2050 kilo watt hours per square meter and year. Concentrating collectors can only use direct irradiation which is about 2000 kilo watt hours per square meter and year.
System efficiencies of stationary solar systems were based according to literature. For flat plate collector operation temperature at 60 °C were assumed and 100 °C for evacuated tube collectors. System efficiencies are assumed at 45 % for FPC and 40 for ETC. According to the pre feasibility study of Fraunhofer system efficiencies at 40 % can be reached by concentrating technologies.
As the system ages an annual degradation of 0.5% is expected. This affects system efficiencies.
The specific solar yield is multiplied by the aperture area of 1000 square meters. The result is the annual solar yield (kWh per year)
The annual solar yield is the amount of heat that is available for processes. But when no process heat is needed it cannot be used. Only few processes operate seven days a week and have a constant high heat demand. The respective utilization rate would be 100%.
For the reference case it is assumed that the process operates seven days a week, in two shifts during the day, but with fluctuating demands. For stationary collectors an utilization rate of 75 % is assumed. Concentrating technologies can be used for steam generation which can be fed in at supply level. Therefore more than one process can be supplied and the utilization rate is higher.
To determine how much fuel is saved, the useful solar yield is divided by the boiler’s efficiency. It is assumed to be 85%.
The resulting fuel savings are then multiplied with the fuel prices. And voila, we get the cash inflow.

## Slide 8
Chart: Cash flows in EUR
Net cash flows | -100500 | -42200.6059 | -40601.6515 | -38842.9746 | -36909.0919 | -34783.0412 | 24746.1266 | 25819.2397 | 26938.6794 | 28106.4348 | 29324.5802 | 30595.2781 | 31920.7832 | 33303.4466 | 34745.7194 | 36250.1569 | 37819.4234 | 39456.2969 | 41163.673 | 42944.571 | 44802.1383
Present Value | -100500 | -37777.604 | -32536.8231 | -27865.0388 | -23702.6146 | -19996.14 | 12735.0769 | 11894.7006 | 11109.6938 | 10376.4136 | 9691.4563 | 9051.6419 | 8453.9996 | 7895.7536 | 7374.3108 | 6887.2484 | 6432.3028 | 6007.3595 | 5610.4429 | 5239.7072 | 4893.4281
Cumulated NCF | -100500 | -142700.6059 | -183302.2574 | -222145.232 | -259054.3238 | -293837.365 | -269091.2384 | -243271.9987 | -216333.3193 | -188226.8844 | -158902.3043 | -128307.0262 | -96386.2429 | -63082.7963 | -28337.077 | 7913.0799 | 45732.5033 | 85188.8002 | 126352.4732 | 169297.0442 | 214099.1824
Chart: Cash flows in EUR
Net cash flows | -120000 | -53297.6325 | -51698.6781 | -49940.0012 | -48006.1185 | -45880.0678 | 24746.1266 | 25819.2397 | 26938.6794 | 28106.4348 | 29324.5802 | 30595.2781 | 31920.7832 | 33303.4466 | 34745.7194 | 36250.1569 | 37819.4234 | 39456.2969 | 41163.673 | 42944.571 | 44802.1383
Present Value | -120000 | -47711.5627 | -41429.6139 | -35825.7853 | -30829.0035 | -26375.6195 | 12735.0769 | 11894.7006 | 11109.6938 | 10376.4136 | 9691.4563 | 9051.6419 | 8453.9996 | 7895.7536 | 7374.3108 | 6887.2484 | 6432.3028 | 6007.3595 | 5610.4429 | 5239.7072 | 4893.4281
Cumulated NCF | -120000 | -173297.6325 | -224996.3106 | -274936.3118 | -322942.4302 | -368822.498 | -344076.3714 | -318257.1317 | -291318.4523 | -263212.0174 | -233887.4372 | -203292.1592 | -171371.3759 | -138067.9293 | -103322.2099 | -67072.0531 | -29252.6296 | 10203.6672 | 51367.3402 | 94311.9112 | 139114.0495
3. Reference Case
Flat Plate Collectors
without grants
current grants at 16.25%
Natural Gas
Fuel Oil
NPV: -178,518 EUR IRR: 2.8 %
Chart: Cash flows in EUR
Net cash flows | -100500 | -48020.4956 | -46971.5208 | -45814.7965 | -44539.751 | -43134.7976 | 15605.1292 | 16269.1827 | 16961.2573 | 17682.5231 | 18434.1985 | 19217.5517 | 20033.9037 | 20884.6292 | 21771.1598 | 22694.9858 | 23657.6585 | 24660.7929 | 25706.0703 | 26795.2405 | 27930.1253
Present Value | -100500 | -42987.5171 | -37641.4261 | -32866.4603 | -28602.9403 | -24797.4134 | 8030.8536 | 7495.0719 | 6994.9374 | 6528.0842 | 6092.303 | 5685.5308 | 5305.8414 | 4951.4361 | 4620.6354 | 4311.8711 | 4023.6791 | 3754.6922 | 3503.6339 | 3269.3123 | 3050.6147
Cumulated NCF | -100500 | -148520.4956 | -195492.0164 | -241306.8129 | -285846.5639 | -328981.3614 | -313376.2322 | -297107.0495 | -280145.7921 | -262463.269 | -244029.0705 | -224811.5188 | -204777.6151 | -183892.9859 | -162121.826 | -139426.8402 | -115769.1817 | -91108.3888 | -65402.3185 | -38607.078 | -10676.9527
Chart: Cash flows in EUR
Net cash flows | -120000 | -59117.5222 | -58068.5474 | -56911.8231 | -55636.7776 | -54231.8241 | 15605.1292 | 16269.1827 | 16961.2573 | 17682.5231 | 18434.1985 | 19217.5517 | 20033.9037 | 20884.6292 | 21771.1598 | 22694.9858 | 23657.6585 | 24660.7929 | 25706.0703 | 26795.2405 | 27930.1253
Present value | -120000 | -52921.4758 | -46534.2168 | -40827.2068 | -35729.3292 | -31176.8929 | 8030.8536 | 7495.0719 | 6994.9374 | 6528.0842 | 6092.303 | 5685.5308 | 5305.8414 | 4951.4361 | 4620.6354 | 4311.8711 | 4023.6791 | 3754.6922 | 3503.6339 | 3269.3123 | 3050.6147
Cumulated NCF | -120000 | -179117.5222 | -237186.0695 | -294097.8927 | -349734.6702 | -403966.4944 | -388361.3652 | -372092.1824 | -355130.9251 | -337448.4019 | -319014.2035 | -299796.6517 | -279762.7481 | -258878.1189 | -237106.959 | -214411.9732 | -190754.3147 | -166093.5218 | -140387.4515 | -113592.211 | -85662.0857
NPV: -118,725 EUR IRR: 4.9 %
Notes: These are the results for the reference case using flat plate collectors.
The left column shows the cash flows without any grants. The right column shows the cash flows with current grants. Those are capped at 65 EUR per square meter which represents 16.25 % of the investment costs of a solar system using flat plate collectors. Above we see the replacement for natural gas, below for fuel oil.
The graphs show the yearly net cash flows in blue. The discounted net cash flows or rather present values are shown in grey. The red line are the cumulated net cash flows.
Only if fuel oil is replaced the payback period is below the life time of the solar system. But, the NPV is negative for both cases and the internal rate of return is also very low.

## Slide 9
3. Reference Case
Evacuated Tube Collectors
without grants
current grants at 13%
Natural Gas
Fuel Oil
Chart: Cash flows in EUR
Net cash flows | -150000 | -78716.9677 | -77858.7694 | -76908.4471 | -75856.7835 | -74693.6679 | 11953.7314 | 12449.6221 | 12965.7751 | 13503.0019 | 14062.1454 | 14644.0816 | 15249.7202 | 15880.0064 | 16535.9218 | 17218.486 | 17928.7581 | 18667.8378 | 19436.8671 | 20237.0319 | 21069.5635
Present value | -150000 | -70466.7237 | -62393.4475 | -55172.3158 | -48714.3955 | -42940.0361 | 6151.7381 | 5735.4333 | 5347.1735 | 4985.0767 | 4647.3868 | 4332.4654 | 4038.7834 | 3764.9142 | 3509.5266 | 3271.3787 | 3049.3115 | 2842.2438 | 2649.1667 | 2469.1392 | 2301.2829
Cumulated NCF | -150000 | -228716.9677 | -306575.7371 | -383484.1843 | -459340.9677 | -534034.6357 | -522080.9043 | -509631.2822 | -496665.507 | -483162.5052 | -469100.3597 | -454456.2782 | -439206.558 | -423326.5516 | -406790.6298 | -389572.1438 | -371643.3857 | -352975.5479 | -333538.6807 | -313301.6488 | -292232.0853
Chart: Cash flows in EUR
Net cash flows | -150000 | -73543.7324 | -72196.6634 | -70711.2721 | -69073.9754 | -67269.8845 | 20079.0624 | 20938.5617 | 21834.5947 | 22768.7011 | 23742.4847 | 24757.6161 | 25815.8354 | 26918.9552 | 28068.8636 | 29267.527 | 30516.9936 | 31819.3969 | 33176.9584 | 34591.9923 | 36066.9084
Present value | -150000 | -65835.6898 | -57856.0226 | -50726.6078 | -44358.5505 | -38672.2375 | 10333.2699 | 9646.2144 | 9004.7347 | 8405.8139 | 7846.6341 | 7324.5641 | 6837.1462 | 6382.0853 | 5957.2381 | 5560.6029 | 5190.3103 | 4844.6147 | 4521.8858 | 4220.6013 | 3939.3393
Cumulated NCF | -150000 | -223543.7324 | -295740.3958 | -366451.6679 | -435525.6433 | -502795.5277 | -482716.4653 | -461777.9037 | -439943.309 | -417174.6078 | -393432.1231 | -368674.507 | -342858.6716 | -315939.7164 | -287870.8529 | -258603.3259 | -228086.3323 | -196266.9354 | -163089.977 | -128497.9847 | -92431.0763
Chart: Cash flows in EUR
Net cash flows | -130500 | -62446.7058 | -61099.6368 | -59614.2455 | -57976.9488 | -56172.8579 | 20079.0624 | 20938.5617 | 21834.5947 | 22768.7011 | 23742.4847 | 24757.6161 | 25815.8354 | 26918.9552 | 28068.8636 | 29267.527 | 30516.9936 | 31819.3969 | 33176.9584 | 34591.9923 | 36066.9084
Present value | -130500 | -55901.7311 | -48963.2318 | -42765.8613 | -37232.1615 | -32292.758 | 10333.2699 | 9646.2144 | 9004.7347 | 8405.8139 | 7846.6341 | 7324.5641 | 6837.1462 | 6382.0853 | 5957.2381 | 5560.6029 | 5190.3103 | 4844.6147 | 4521.8858 | 4220.6013 | 3939.3393
Cumulated NCF | -130500 | -192946.7058 | -254046.3426 | -313660.5881 | -371637.5369 | -427810.3948 | -407731.3324 | -386792.7707 | -364958.176 | -342189.4748 | -318446.9901 | -293689.374 | -267873.5386 | -240954.5834 | -212885.7199 | -183618.1929 | -153101.1993 | -121281.8024 | -88104.844 | -53512.8517 | -17445.9433
Chart: Cash flows in EUR
Net cash flows | -130500 | -67619.9411 | -66761.7428 | -65811.4205 | -64759.7569 | -63596.6413 | 11953.7314 | 12449.6221 | 12965.7751 | 13503.0019 | 14062.1454 | 14644.0816 | 15249.7202 | 15880.0064 | 16535.9218 | 17218.486 | 17928.7581 | 18667.8378 | 19436.8671 | 20237.0319 | 21069.5635
Present value | -130500 | -60532.765 | -53500.6567 | -47211.5693 | -41588.0066 | -36560.5566 | 6151.7381 | 5735.4333 | 5347.1735 | 4985.0767 | 4647.3868 | 4332.4654 | 4038.7834 | 3764.9142 | 3509.5266 | 3271.3787 | 3049.3115 | 2842.2438 | 2649.1667 | 2469.1392 | 2301.2829
Cumulated NCF | -130500 | -198119.9411 | -264881.6839 | -330693.1045 | -395452.8614 | -459049.5027 | -447095.7713 | -434646.1492 | -421680.3741 | -408177.3722 | -394115.2268 | -379471.1452 | -364221.425 | -348341.4186 | -331805.4968 | -314587.0108 | -296658.2527 | -277990.4149 | -258553.5478 | -238316.5159 | -217246.9523
Notes: For evacuated tube collectors, economics are even less attractive. 65 EUR per square meters represent 13 %, since the investment is higher using evacuated tube collectors.
I didn‘t mention the net present value and the internal rate of return, as the investment is obviously not feasible.
(The first net cash flow represents the cash outflow for the initial investment financed by equity. During the subsequent five years, net cash flow the loan is paid back and after that net cash flows are positive.)

## Slide 10
3. Reference Case
Concentrating Technologies
without grants
current grants at 11.8%
Natural Gas
Fuel Oil
Chart: Cash flows in EUR
Net cash flows | -165000 | -82888.3021 | -81466.8157 | -79892.6951 | -78150.6608 | -76223.9516 | 19803.7337 | 20627.2849 | 21484.595 | 22377.0217 | 23305.9761 | 24272.9244 | 25279.3903 | 26326.9567 | 27417.2683 | 28552.0338 | 29733.0283 | 30962.0956 | 32241.1512 | 33572.1844 | 34957.2614
Present value | -165000 | -74200.8648 | -65284.8166 | -57313.1453 | -50187.4984 | -43819.7684 | 10191.5777 | 9502.8119 | 8860.3925 | 8261.2125 | 7702.3728 | 7181.1676 | 6695.0724 | 6241.7313 | 5818.9458 | 5424.6647 | 5056.974 | 4714.0876 | 4394.3391 | 4096.1736 | 3818.1402
Cumulated NCF | -165000 | -247888.3021 | -329355.1178 | -409247.8129 | -487398.4736 | -563622.4253 | -543818.6916 | -523191.4067 | -501706.8117 | -479329.79 | -456023.8139 | -431750.8895 | -406471.4992 | -380144.5425 | -352727.2743 | -324175.2405 | -294442.2122 | -263480.1166 | -231238.9654 | -197666.7809 | -162709.5195
Chart: Cash flows in EUR
Net cash flows | -145530 | -71808.3478 | -70386.8614 | -68812.7409 | -67070.7065 | -65143.9974 | 19803.7337 | 20627.2849 | 21484.595 | 22377.0217 | 23305.9761 | 24272.9244 | 25279.3903 | 26326.9567 | 27417.2683 | 28552.0338 | 29733.0283 | 30962.0956 | 32241.1512 | 33572.1844 | 34957.2614
Present value | -145530 | -64282.1891 | -56405.7071 | -49364.646 | -43072.0732 | -37450.1035 | 10191.5777 | 9502.8119 | 8860.3925 | 8261.2125 | 7702.3728 | 7181.1676 | 6695.0724 | 6241.7313 | 5818.9458 | 5424.6647 | 5056.974 | 4714.0876 | 4394.3391 | 4096.1736 | 3818.1402
Cumulated NCF | -145530 | -217338.3478 | -287725.2093 | -356537.9501 | -423608.6566 | -488752.654 | -468948.9203 | -448321.6354 | -426837.0404 | -404460.0187 | -381154.0426 | -356881.1182 | -331601.7279 | -305274.7713 | -277857.503 | -249305.4692 | -219572.441 | -188610.3454 | -156369.1941 | -122797.0097 | -87839.7483
Chart: Cash flows in EUR
Net cash flows | -145530 | -77864.8184 | -77015.6685 | -76067.9702 | -75011.555 | -73835.256 | 10291.151 | 10689.0142 | 11101.5867 | 11529.3738 | 11972.8959 | 12432.6889 | 12909.3042 | 13403.3093 | 13915.2876 | 14445.8395 | 14995.5818 | 15565.1484 | 16155.1907 | 16766.3771 | 17399.3942
Present value | -145530 | -69703.8873 | -61717.8142 | -54569.3774 | -48171.5991 | -42446.5506 | 5296.1258 | 4924.3365 | 4578.3695 | 4256.447 | 3956.9125 | 3678.2228 | 3418.9403 | 3177.726 | 2953.3323 | 2744.5974 | 2550.4388 | 2369.8484 | 2201.8874 | 2045.6813 | 1900.4157
Cumulated NCF | -145530 | -223394.8184 | -300410.4869 | -376478.4571 | -451490.0121 | -525325.2682 | -515034.1171 | -504345.1029 | -493243.5162 | -481714.1425 | -469741.2465 | -457308.5576 | -444399.2534 | -430995.9441 | -417080.6565 | -402634.817 | -387639.2352 | -372074.0868 | -355918.8961 | -339152.519 | -321753.1247
Chart: Cash flows in EUR
Net cash flows | -165000 | -88944.7727 | -88095.6227 | -87147.9244 | -86091.5093 | -84915.2103 | 10291.151 | 10689.0142 | 11101.5867 | 11529.3738 | 11972.8959 | 12432.6889 | 12909.3042 | 13403.3093 | 13915.2876 | 14445.8395 | 14995.5818 | 15565.1484 | 16155.1907 | 16766.3771 | 17399.3942
Present value | -165000 | -79622.563 | -70596.9238 | -62517.8766 | -55287.0244 | -48816.2155 | 5296.1258 | 4924.3365 | 4578.3695 | 4256.447 | 3956.9125 | 3678.2228 | 3418.9403 | 3177.726 | 2953.3323 | 2744.5974 | 2550.4388 | 2369.8484 | 2201.8874 | 2045.6813 | 1900.4157
Cumulated NCF | -165000 | -253944.7727 | -342040.3954 | -429188.3198 | -515279.8291 | -600195.0394 | -589903.8884 | -579214.8741 | -568113.2875 | -556583.9137 | -544611.0178 | -532178.3289 | -519269.0246 | -505865.7154 | -491950.4278 | -477504.5883 | -462509.0065 | -446943.858 | -430788.6673 | -414022.2902 | -396622.896
Notes: These are the results for concentrating technologies. Higher O&M costs have a big impact and can not be compensated by the higher utiliziation rate.
The technical potential is higher for concentrating technologies as they can supply process heat at higher temperatures. But economics are not attractive under current conditions.
 If you any doubts about the input parameters, I can open the calculation tool. So, we can modify some parameters.

## Slide 11
4. Sensitivity Analysis
Concentrating Technologies
Chart: Change of input parameter in %
| -0.9 | -0.85 | -0.8 | -0.75 | -0.7 | -0.65 | -0.6 | -0.55000000000000004 | -0.5 | -0.45 | -0.4 | -0.35 | -0.29999999999999899 | -0.249999999999999 | -0.19999999999999901 | -0.149999999999999 | -9.9999999999999006E-2 | -4.9999999999998997E-2 | 9.9920072216264108E-16 | 5.0000000000000898E-2 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5
Annual inflation rate | 28.2912 | 28.5184 | 28.7657 | 29.0333 | 29.3088 | 29.6128 | 29.9499 | 30.3033 | 30.6968 | 31.1332 | 31.6087 | 32.1489 | 32.7522 | 33.4416 | 34.2461 | 35.1974 | 36.3523 | 37.8224 | 39.8099 | 42.875
Natural gas price | 31.6087 | 30.3117 | 29.1336 | 28.0544 | 27.0596 | 26.1389 | 25.2844 | 24.4908 | 23.754 | 23.0665 | 22.4114 | 21.8042 | 21.2282 | 20.6838 | 20.1721 | 19.6825 | 19.2213 | 18.7816 | 18.3605 | 17.9678 | 17.5792 | 17.217 | 16.87 | 16.5311 | 16.2131 | 15.9081
Annual energy price increase | 55.1281 | 49.9021 | 45.3808 | 41.5421 | 38.3201 | 35.6386 | 33.4279 | 31.6087 | 30.0776 | 28.746 | 27.5791 | 26.5438 | 25.6151 | 24.7766 | 24.0168 | 23.3031
Interest rate | 31.2727 | 31.3562 | 31.4401 | 31.5242 | 31.6087 | 31.6935 | 31.7787 | 31.8641 | 31.9499 | 32.0335 | 32.1139 | 32.1946 | 32.2756 | 32.3569 | 32.4385 | 32.5203 | 32.6024 | 32.6848 | 32.7675
Boiler efficiency | 28.8858 | 30.2477 | 31.6087 | 32.979 | 34.3356
Specific total investment cost | 25.3681 | 26.6593 | 27.9324 | 29.1756 | 30.3992 | 31.6087 | 32.8051 | 33.9891 | 35.1501 | 36.3 | 37.4403 | 38.5716 | 39.6944 | 40.8091 | 41.9163 | 43.015 | 44.1011 | 45.1809 | 46.255 | 47.3233 | 48.3862 | 49.4438
O&M costs | 26.4708 | 26.9236 | 27.3784 | 27.8567 | 28.3421 | 28.8495 | 29.3653 | 29.9061 | 30.4524 | 31.0294 | 31.6087 | 32.2159 | 32.8408 | 33.4788 | 34.1452 | 34.8263 | 35.524 | 36.2486 | 36.999 | 37.7558 | 38.5381 | 39.3448 | 40.175 | 41.0277 | 41.8931 | 42.7782 | 43.6843 | 44.6102 | 45.555 | 46.5176 | 47.4969
System efficiency | 46.6398 | 43.4667 | 40.7783 | 38.4551 | 36.4284 | 34.639 | 33.0497 | 31.6087 | 30.3117 | 29.1336 | 28.0544 | 27.0596 | 26.1389
Utilization rate | 43.4667 | 40.7783 | 38.4551 | 36.4284 | 34.639 | 33.0497 | 31.6087 | 30.3117 | 29.1336
Notes: The graph illustrates the results of the sensitivity analysis for concentrating technologies. It shows how different input parameters influence the payback time. The payback period is about 32 years for unvaried reference parameters.
I will just mention the most interesting aspects of this graph:
If natural gas prices were not subsidized and as a result more than twice as high, the payback period would decrease by around 50% to 16 years.
Varied interest rates have a small impact, which shows the limitations of soft loans as a financial policy instrument.
Investment costs impact various factors, such as equity investment, loan repayments, and O&M costs. They have the strongest relative impact. If they were at 400 EUR/m² (20% less than the reference case) the payback period would be about 25 years.
For stationary technologies the graph is very similar (only the curves are not as steep).

## Slide 12
5. Policy Instruments
Grants
Value | Unit | Replaced fuel | FPC |  | ETC |  | Concentrating | 
 |  |  | 0% | 50% | 0% | 50% | 0% | 50%
SPP | a | NG | 22.8 | 14.3 | 30.8 | 20.2 | 36.4 | 24.1
 |  | FO | 16.7 | 10.1 | 22.4 | 14.0 | 24.2 | 15.2
Gross Public Costs | EUR/m² | - | 0 | 200 | 0 | 250 | 0 | 275
Public Savings | EUR/m² | NG | 52.81 |  | 46.94 |  | 54.96 | 
 |  | FO | 203.99 |  | 181.33 |  | 212.28 | 
Net Public Costs | EUR/m² | NG | -52.81 | 147.19 | -46.94 | 203.06 | -54.96 | 220.04
 |  | FO | -203.99 | -3.99 | -181.33 | 68.67 | -212.28 | 62.72
Notes: The barrier of high investment costs can be tackled by providing grants. Current grants are very low and do not yield economic feasible SHIP investments.
A maximum grant rate of 50% is assumed, but payback periods are still above 14 years for all technologies. If fuel oil is replaced a payback period of 10 years can be reached. Almost all options yield negative NPV negative, so they are not mentioned here. Only FPC and FO replacement shows a NPV slightly above zero (5,400 EUR).
A 50% grant causes public costs. 200 EUR/m² is 50% of the total investment cost.
Since energy prices are highly subsidized, the Tunisian state saves public spendings if the consumption of conventional energy is reduced. I called that public savings. A 1000 square meter plant results in public savings at about 50 EUR per square meter if natural gas is replaced. Subsidies for fuel oil are even higher, therefore public savings are significantly higher if fuel oil is replaced. About 200 EUR/m².
Negative net public costs indicate public savings! Highlighted in green. For fuel oil replacement, it could be justified to provide grants even above 50%. The net public costs for FPC and FO replacement are around zero. Even for concentrating technologies, net public costs of a 50% grant are not that high.
If there are questions about the calculation, I can show you the details later.

## Slide 13
Soft Loans
Interest rate: 5.5%
Grace period: 3 years
Repayment period: 12 years
Chart: Cash flows in EUR
Net cash flows | -120000 | -53297.6325 | -51698.6781 | -49940.0012 | -48006.1185 | -45880.0678 | 24746.1266 | 25819.2397 | 26938.6794 | 28106.4348 | 29324.5802 | 30595.2781 | 31920.7832 | 33303.4466 | 34745.7194 | 36250.1569 | 37819.4234 | 39456.2969 | 41163.673 | 42944.571 | 44802.1383
Present value | -120000 | -47711.5627 | -41429.6139 | -35825.7853 | -30829.0035 | -26375.6195 | 12735.0769 | 11894.7006 | 11109.6938 | 10376.4136 | 9691.4563 | 9051.6419 | 8453.9996 | 7895.7536 | 7374.3108 | 6887.2484 | 6432.3028 | 6007.3595 | 5610.4429 | 5239.7072 | 4893.4281
Cumulated NCF | -120000 | -173297.6325 | -224996.3106 | -274936.3118 | -322942.4302 | -368822.498 | -344076.3714 | -318257.1317 | -291318.4523 | -263212.0174 | -233887.4372 | -203292.1592 | -171371.3759 | -138067.9293 | -103322.2099 | -67072.0531 | -29252.6296 | 10203.6672 | 51367.3402 | 94311.9112 | 139114.0495
NPV: -178,518 EUR IRR: 2.8 % SPP: 16.7 a
Chart: Cash flows in EUR
Net cash flows | -120000 | -17496.4228 | -15897.4684 | -14138.7915 | -12204.9088 | -10078.8581 | -7742.0581 | -6668.945 | -5549.5053 | -4381.7499 | -3163.6045 | -1892.9067 | -567.4015 | 33303.4466 | 34745.7194 | 36250.1569 | 37819.4234 | 39456.2969 | 41163.673 | 42944.571 | 44802.1383
Present value | -120000 | -15662.6408 | -12739.7063 | -10142.8373 | -7837.8587 | -5794.1528 | -3984.2884 | -3072.3253 | -2288.6536 | -1617.6669 | -1045.537 | -560.0182 | -150.2724 | 7895.7536 | 7374.3108 | 6887.2484 | 6432.3028 | 6007.3595 | 5610.4429 | 5239.7072 | 4893.4281
Cumulated NCF | -120000 | -137496.4228 | -153393.8911 | -167532.6826 | -179737.5914 | -189816.4494 | -197558.5076 | -204227.4526 | -209776.9579 | -214158.7078 | -217322.3124 | -219215.219 | -219782.6205 | -186479.1739 | -151733.4545 | -115483.2977 | -77663.8742 | -38207.5774 | 2956.0956 | 45900.6666 | 90702.8049
NPV: -134,555 EUR IRR: 2.36 % SPP: 17.9 a
Interest rate: 7.0%
Grace period: 0 years
Repayment period: 5 years
5. Policy Instruments
Notes: The sensitivity analysis has already shown that interest rates have only a small impact on the payback period.
A soft loan with a 5.5 % interest rate, a grace period of 3 years and repayment period of 12 years would only shift loan repayments. This results in even longer payback periods.
It can be concluded that soft loans are not a suitable policy instrument for SHIP investments.

## Slide 14
5. Policy Instruments
Bonus Model
Value | Unit | FPC | ETC | Conc | FPC | ETC | Conc | FPC | ETC | Conc
NG Bonus | EUR/kWh | 0 |  |  | 0.015 |  |  | 0.04 |  | 
SPP | a | 22.8 | 30.8 | 36.4 | 15.4 | 21.7 | 25.5 | 9.2 | 13.2 | 15.3
Net Public Costs | EUR/m² | -52.81 | -46.94 | -54.96 | 58.24 | 51.77 | 60.61 | 243.33 | 216.29 | 253.22
FO Bonus | EUR/kWh |  | 0 |  | 0.035 |  |  | 0.05 |  | 
NPV | EUR | - 178,518 | - 307,434 | - 357,846 | 59,829 | - 95,570 | - 151,150 | 161,977 | - 4,772 | - 62,566
IRR | % | 2.80% | -1.70% | -2.83% | 14.80% | 7.66% | 5.82% | 20.41% | 11.50% | 9.27%
SPP | a | 16.7 | 22.4 | 24.2 | 8.6 | 12.1 | 13.5 | 7.0 | 9.9 | 11.0
Net Public Costs | EUR/m² | -203.99 | -181.33 | -212.28 | 55.13 | 49.00 | 57.37 | 166.18 | 147.72 | 172.94
Notes: Besides the high investment costs, the low energy prices are a large barrier to SHIP investments. Bonus payments for every kilowatt hour of saved conventional energy can compensate to some extent for low energy prices. The Bonus Model has the advantage over the grant that financial support is only granted for used solar process heat. This encourages plant operators to maintain the plant. On the other hand, it requires heat metering of the used solar process heat.
The minimum amount of bonus paid by the Tunisian state should be the subsidy. For natural gas, this is currently about 1.7 EUR cents/kWh and for fuel oil about 4.3 EUR cents/kWh. As subsidies are reduced in the future, public savings will also decrease. Therefore net public costs increase.
Again, fuel oil replacement shows the most attractive investments. For FPC NPV is positive when a bonus is paid at 3.5 or 5 EUR cents/kWh. The payback period however remains above 5 years. 5 years is the maximum acceptable payback time according to interviewed partner companies in Tunisia.

## Slide 15
6. Conclusion
Current grants are not sufficient for economic feasibility
Combination of grants and bonus payments should be considered
Policy instruments should be directed to industries using fuel oil
Identification of most promising industries by energy audits
Maximum payback period five years is large barrier  ESCOs, awareness-raising, demonstration plants
…
Notes: It can be concluded, that current grants are not sufficient for economic feasible SHIP investments. Grant rates above 50% can be justified for SHIP plants replacing fuel oil.
A combination of grants and bonus payments could be an interesting instruments that tackles both barriers: high investment costs and low energy prices
The financial policy instruments should be directed to industries using fuel oil, because fuel oil subsidies cause high public costs and yield more attractive SHIP investments.
The most promising industrial companies need to be identified. This could be done by gathering relevant data from the obligated energy audits already carried out by the ANME (the Tunisian Agency for Energy Conservation)
The main barrier of SHIP investments can be seen in the long payback period due to long lifetimes and high investment costs. It is a big challenge to reach payback period of five years. Energy Service Companies might accept higher payback periods. Awareness-raising and demonstration plants could contribute to reduce skepticism towards SHIP among industries. This can result in higher acceptable payback periods.
These were my conclusions. But everyone is invited to make their own conclusion and if you have any questions now, please don’t hesitate to ask.

## Slide 16
Gas Price

## Slide 17
Energy Subsidies and Public Savings
t |  | Mean cost price (increase by 1 %/a) |  | Industrial retail price (excl. VAT) (increase 2015-21: 10%, then 5%) |  | Total subsidies (mean cost-retail price) |  | Fuel Savings |  |  | Discounted specific public savings, NG |  | 
 |  | EUR cents/kWh |  | EUR cents/kWh |  | EUR cents/kWh |  | kWh/1000m² |  |  | EUR/m² |  | 
 |  | NG | FO | NG | FO | NG | FO | FPC | ETC | Conc | FPC | ETC | Conc
 | 2012 |  | 6.45 |  | 2.15 |  |  |  |  |  |  |  | 
 | 2013 |  | 6.51 |  |  |  |  |  |  |  |  |  | 
0 | 2014 | 3.10 | 6.58 | 1.38 | 2.28 | 1.72 | 4.30 |  |  |  |  |  | 
1 | 2015 | 3.13 | 6.65 | 1.52 | 2.51 | 1.61 | 4.14 | 813,971 | 723,529 | 847,059 | 12.09 | 10.75 | 12.58
2 | 2016 | 3.16 | 6.71 | 1.67 | 2.76 | 1.49 | 3.95 | 809,901 | 719,912 | 842,824 | 10.25 | 9.11 | 10.67
3 | 2017 | 3.19 | 6.78 | 1.84 | 3.03 | 1.36 | 3.74 | 805,851 | 716,312 | 838,609 | 8.54 | 7.60 | 8.89
4 | 2018 | 3.23 | 6.85 | 2.02 | 3.34 | 1.21 | 3.51 | 801,822 | 712,731 | 834,416 | 6.95 | 6.18 | 7.24
5 | 2019 | 3.26 | 6.92 | 2.22 | 3.67 | 1.04 | 3.24 | 797,813 | 709,167 | 830,244 | 5.48 | 4.87 | 5.70
6 | 2020 | 3.29 | 6.98 | 2.44 | 4.04 | 0.85 | 2.95 | 793,824 | 705,621 | 826,093 | 4.10 | 3.64 | 4.27
7 | 2021 | 3.32 | 7.05 | 2.57 | 4.24 | 0.76 | 2.81 | 789,855 | 702,093 | 821,963 | 3.36 | 2.99 | 3.50
8 | 2022 | 3.36 | 7.12 | 2.70 | 4.45 | 0.66 | 2.67 | 785,905 | 698,583 | 817,853 | 2.69 | 2.39 | 2.80
9 | 2023 | 3.39 | 7.20 | 2.83 | 4.68 | 0.56 | 2.52 | 781,976 | 695,090 | 813,764 | 2.09 | 1.86 | 2.17
10 | 2024 | 3.42 | 7.27 | 2.97 | 4.91 | 0.45 | 2.36 | 778,066 | 691,614 | 809,695 | 1.55 | 1.38 | 1.61
11 | 2025 | 3.46 | 7.34 | 3.12 | 5.16 | 0.34 | 2.19 | 774,176 | 688,156 | 805,646 | 1.06 | 0.94 | 1.10
12 | 2026 | 3.49 | 7.41 | 3.28 | 5.41 | 0.22 | 2.00 | 770,305 | 684,715 | 801,618 | 0.62 | 0.55 | 0.65
13 | 2027 | 3.53 | 7.49 | 3.44 | 5.68 | 0.09 | 1.80 | 766,453 | 681,292 | 797,610 | 0.23 | 0.21 | 0.24
14 | 2028 | 3.56 | 7.56 | 3.61 | 5.97 | -0.05 | 1.60 | 762,621 | 677,885 | 793,622 | -0.12 | -0.10 | -0.12
15 | 2029 | 3.60 | 7.64 | 3.79 | 6.27 | -0.19 | 1.37 | 758,808 | 674,496 | 789,654 | -0.43 | -0.38 | -0.45
16 | 2030 | 3.63 | 7.72 | 3.98 | 6.58 | -0.35 | 1.14 | 755,014 | 671,123 | 785,705 | -0.70 | -0.62 | -0.73
17 | 2031 | 3.67 | 7.79 | 4.18 | 6.91 | -0.51 | 0.88 | 751,239 | 667,768 | 781,777 | -0.95 | -0.84 | -0.98
18 | 2032 | 3.71 | 7.87 | 4.39 | 7.25 | -0.68 | 0.62 | 747,483 | 664,429 | 777,868 | -1.16 | -1.03 | -1.21
19 | 2033 | 3.75 | 7.95 | 4.61 | 7.62 | -0.86 | 0.33 | 743,745 | 661,107 | 773,979 | -1.35 | -1.20 | -1.40
20 | 2034 | 3.78 | 8.03 | 4.84 | 8.00 | -1.06 | 0.03 | 740,026 | 657,801 | 770,109 | -1.51 | -1.34 | -1.57
 |  |  |  |  |  |  |  |  |  |  | 52.81 | 46.94 | 54.96

## Slide 18
Plant (Country) | Process (Temp. in °C) | Col-lector | Specific system costs in EUR/m² | Aperture area in m² | Year | PP (incl. subsidy) | Source
Benetton Textiles (TUN) | Dyeing (60) | FPC | 345 | 869 | 2014 | n.a. | Frein et al. (2014, p. 1162)
Göss Brewery (AUT) | Brewing (80) | FPC | 815 | 1375 | 2013 | 10 (50%) | Mauthner et al. (2013)
LEITL Con-crete (AUT) | Drying (45) | FPC | 1,045 | 287 | 2010 | n.a. | SO-PRO (2010b)
Montesano Meat (ESP) | Washing (40-45) | FPC | 763 | 229 | 2011 | 7 (33%) | SO-PRO (2014)
Merl Food (DEU) | Washing (60) | FPC | 575 | 517 | 2010 | 9 (30%) | SO-PRO (2010a)
Steinbach Metal (DEU) | Preheating (60-80) | ETC | 600 | 400 | 2008 | 7 (50%) | ESV (2011)
Hustert Gal-vanik (DEU) | Heating Baths (80) | ETC | 724 | 221 | 2011 | (30%) | SO-PRO (2014) ESV (2011)
El Nasr Pharma (EGY) | Steam (175) | PTC | 1025 | 1900 | 2003 | n.a. | Cottret (2011)
Emmy Dairy (CHE) | Steam (140-180) | PTC | 957 | 627 | 2012 | 10 (50%) | Minder (2014)
Cremo Dairy (CHE) | Superheated water (125-170) | PTC | 1205 | 581 | 2013 | 10 (50%) | Minder (2014)
System Costs

## Slide 19
GHI in kWh/m²/a |  |  | DNI in kWh/m²/a |  |  | Source
North | Center | Average | North | Center | Average | 
1743 | 1891 | 1817 | 1853 | 2040 | 1947 | Solar Med Atlas
1719 | 1820 | 1770 | 1814 | 1888 | 1851 | SoDa, 2005
1856 (2112) | 2047 (2332) | 1952 (2222) | 2113 | 2311 | 2212 | PVGIS (optimal inclination angle: 31°)
- | - | - | 1800 | 2250 | 2025 | Trieb et al.
1716 | - | - | - | - | - | El Ouderni et al.
1759 (1988) | 1919 (2168) | 1839 (2078) | 1895 | 2122 | 2009 | Total Average (Irradiation at optimal angle)
Solar Irradiation

## Slide 20
Detailed Economics
 | Unit | FPC |  |  | ETC |  |  | Concentrating |  | 
Grant rate | % | 0 | 16.25 | 50 | 0 | 13 | 50 | 0 | 11.8 | 50
Natural Gas Replacement |  |  |  |  |  |  |  |  |  | 
NPV | EUR | - 249,571 | - 189,777 | - 65,591 | - 370,592 | - 310,799 | - 140,617 | - 431,787 | - 372,086 | - 178,815
IRR | % | -1.99% | -0.28% | 5.45% | -6.34% | -5.19% | -0.13% | -8.50% | -7.53% | -2.75%
SPP | a | 22.8 | 20.4 | 14.3 | 30.8 | 28.5 | 20.2 | 36.4 | 33.9 | 24.1
Fuel Oil Replacement |  |  |  |  |  |  |  |  |  | 
NPV | EUR | - 178,518 | - 118,725 | 5,462 | - 307,434 | - 247,641 | - 77,460 | - 357,846 | - 298,145 | - 104,875
IRR | % | 2.80% | 4.87% | 12.19% | -1.70% | -0.35% | 5.83% | -2.83% | -1.66% | 4.32%
SPP | a | 16.7 | 14.8 | 10.1 | 22.4 | 20.5 | 14.0 | 24.2 | 22.3 | 15.2

## Slide 21
Input parameter | Unit | Minimum |  | Reference | Maximum | 
 |  | absolute | relative | absolute | absolute | relative
Annual inflation | %/a | 2 | 45% | 4.4 | 6.5 | 148%
Natural gas price | EUR/kWh | - | - | 0.0163 | 0.037 | 227%
Annual energy price increase | %/a | 1 | 14% | 7 | 10 | 143%
Interest rate | % | 5.5 | 79% | 7 | 12 | 171%
Boiler efficiency | % | 75 | 88% | 85 | 95 | 112%
Specific Total Investment Costs | EUR/m² | 400 | 73% | 550 | 1000 | 182%
O&M | % of Cinv | 0.75 | 50% | 1.5 | 3 | 200%
System efficiency | % of G | 25 | 63% | 40 | 50 | 125%
Utilization rate | % of Qsol | 60 | 67% | 90 | 100 | 111%
Sensitivity Analysis - Ranges